## Slide 1
EMBEDDED SERIAL PROTOCOLS
SBUS vs IBUS
RC Receiver Communication Protocols — From Basics to Implementation
25 vs 32
PACKET BYTES
16 vs 14
CHANNELS
100k vs 115.2k
BAUD RATE
Prepared for team knowledge-share | STM32CubeIDE | HAL Driver

## Slide 2
AGENDA
What we'll cover
01
What is SBUS & IBUS
Origins, purpose, and where they're used in RC/flight-control systems
02
Protocol Fundamentals
Baud rate, framing, parity, signal polarity — the wire-level basics
03
Packet Structure
Byte-by-byte breakdown of both packet formats
04
Side-by-Side Comparison
Every key difference in one table
05
STM32 Implementation
Real code: sbus.c / sbus.h and ibus.c / ibus.h
06
Worked Examples
Actual channel values → actual packet bytes, hand-verified
07
Debugging Lessons
Real build errors we hit and how we fixed them
02

## Slide 3
01 — BASICS
What is SBUS?
SBUS (Serial BUS) is a serial protocol developed by Futaba to send RC receiver channel data to a flight controller or servo controller using a single wire, instead of one wire per channel.
Carries 16 proportional channels in one continuous frame
Signal is inverted (idle HIGH) — most flight controllers invert it internally
Uses UART 8E2 framing: 8 data bits, Even parity, 2 stopbits
Very common in FPV drones and fixed-wing setups (Futaba, FrSky, many others)
Frame size
25 bytes
Refresh rate
~7 ms typical
Channel resolution
11-bit (172–1811)
Center value ≈ 992
03

## Slide 4
01 — BASICS
What is IBUS?
IBUS is a serial protocol developed by FlySky, serving the same purpose as SBUS — one wire carrying all RC channel data — but with a simpler, non-inverted, checksum-protected frame.
Carries 14 channels, each a plain 16-bit value (no bit-packing)
Signal is normal / non-inverted — no inverter circuit needed on the PCB
Uses standard UART 8N1 framing: 8 data bits, No parity, 1 stop bit
Includes a 2-byte checksum for error detection — SBUS has none
Common on FlySky receivers (FS-iA6B, FS-X6B, etc.)
Frame size
32 bytes
Refresh rate
~7 ms typical
Channel resolution
16-bit (1000–2000)
Center value = 1500
04

## Slide 5
02 — HOW IT WORKS
SBUS: 11-bit channels packed into a byte stream
Each of the 16 channels only needs 11 bits (0–2047), not a full byte or word. SBUS squeezes them together edge-to-edge so no bits are wasted — this is called bit-packing.
The "bucket" technique
A 32-bit accumulator holds bits until it has 8+ — then the lowest byte is peeled off into the packet, and the bucket keeps the leftover bits for the next channel.
bucket |= ((uint32_t)(channel[i] & 0x07FF)) << bitInBucket;
bitInBucket += 11;
while (bitInBucket >= 8) {
sbusPacket[byteIndex++] = (uint8_t)(bucket & 0xFF);
bucket >>= 8;
bitInBucket -= 8;
}
05

## Slide 6
02 — HOW IT WORKS
IBUS: plain 16-bit values + checksum
IBUS doesn't bit-pack. Each channel gets its own 2 bytes (low byte, then high byte — little-endian). The trade-off for the simpler layout is a larger frame, made safe with a checksum.
Why the checksum matters
Start from 0xFFFF, subtract every byte in the frame (except the checksum itself). The receiver repeats the same sum — if it doesn't match, the packet is dropped instead of driving a servo with corrupted data.
ibusPacket[2 + i*2] = (uint8_t)(val & 0xFF); // low byte
ibusPacket[2 + i*2 + 1] = (uint8_t)((val >> 8) & 0xFF); // high byte
checksum = 0xFFFF;
for (i = 0; i < 30; i++) checksum -= ibusPacket[i];
ibusPacket[30] = checksum & 0xFF;
ibusPacket[31] = (checksum >> 8) & 0xFF;
06

## Slide 7
03 — PACKET STRUCTURE
SBUS Frame — 25 Bytes
Byte 0
Start
0x0F
Byte 1–22
16 channels
(11-bit packed)
Byte 23
failsafe
Flags
(etc.)
Byte 24
End
0x00
Field-by-field
Start byte
0x0F
Fixed marker — tells receiver a new frame begins
Channel data
22 bytes
16 channels × 11 bits, bit-packed with no gaps
Flag byte
1 byte
Digital ch17/18, frame-lost, failsafe bits
End byte
0x00
Fixed marker — closes the frame
07

## Slide 8
03 — PACKET STRUCTURE
IBUS Frame — 32 Bytes
Byte 0–1
Header
0x20 0x40
Byte 2–29
14 channels (16-bit each)
Byte 30–31
Checksum
0xFFFF − sum
Field-by-field
Length byte
0x20 (32)
Fixed — states total frame length
Command byte
0x40 (64)
Fixed — identifies this as channel-data frame
Channel data
28 bytes
14 channels × 2 bytes, little-endian, no packing
Checksum
2 bytes
0xFFFF minus sum of bytes 0–29, little-endian
08

## Slide 9
04 — COMPARISON
SBUS vs IBUS — Side by Side
Parameter
SBUS
IBUS
Developer
Futaba
FlySky
Baud rate
100,000
115,200
Frame format
8E2 (8 data, Even parity, 2 stop)
8N1 (8 data, No parity, 1 stop)
Signal polarity
Inverted (idle HIGH)
Normal / non-inverted
Channels
16
14
Channel encoding
11-bit, bit-packed
16-bit, plain (unpacked)
Channel range
172 – 1811 (mid ≈ 992)
1000 – 2000 (mid = 1500)
Frame size
25 bytes
32 bytes
Error checking
None
16-bit checksum
Extra hardware
Signal inverter often needed
None — direct UART connection
09

## Slide 10
05 — STM32 IMPLEMENTATION
UART Configuration on STM32CubeMX
SBUS — huart2.Init
IBUS — huart2.Init
BaudRate
115200
WordLength
UART_WORDLENGTH_8B
StopBits
UART_STOPBITS_2
Parity
UART_PARITY_EVEN
Mode
UART_MODE_TX_RX
BaudRate
115200
WordLength
UART_WORDLENGTH_8B
StopBits
UART_STOPBITS_1
Parity
UART_PARITY_NONE
Mode
UART_MODE_TX_RX
⚠ Needs a hardware signal inverter — SBUS idles HIGH, UART idles LOW.
✓ Direct TX-to-RX wiring — no inverter circuit required.
10

## Slide 11
05 — STM32 IMPLEMENTATION
sbus.c — updateSbusPacket()
#include "sbus.h"
uint8_t sbusPacket[25];
void updateSbusPacket(uint16_t *channel)
{
sbusPacket[0] = 0x0F; // start byte
sbusPacket[24] = 0x00; // end byte
uint32_t bucket = 0;
uint8_t bitInBucket = 0;
uint8_t byteIndex = 1;
for (int i = 0; i < 16; i++) {
bucket |= ((uint32_t)(channel[i] & 0x07FF)) << bitInBucket;
bitInBucket += 11;
while (bitInBucket >= 8) {
sbusPacket[byteIndex++] = (uint8_t)(bucket & 0xFF);
bucket >>= 8;
bitInBucket -= 8;
}
}
sbusPacket[23] = 0x00; // flag byte
}
11

## Slide 12
05 — STM32 IMPLEMENTATION
ibus.c — updateIbusPacket()
#include "ibus.h"
uint8_t ibusPacket[IBUS_PACKET_LEN];
void updateIbusPacket(uint16_t *channel, uint8_t num_of_channels)
{
ibusPacket[0] = 0x20; // length
ibusPacket[1] = 0x40; // command: channel data
uint16_t checksum = 0xFFFF;
for (int i = 0; i < IBUS_NUM_CHANNELS; i++) {
uint16_t val = (i < num_of_channels) ? channel[i] : 1500;
ibusPacket[2 + i*2] = (uint8_t)(val & 0xFF);
ibusPacket[2 + i*2 + 1] = (uint8_t)((val >> 8) & 0xFF);
}
for (int i = 0; i < 30; i++)
checksum -= ibusPacket[i];
ibusPacket[30] = (uint8_t)(checksum & 0xFF);
ibusPacket[31] = (uint8_t)((checksum >> 8) & 0xFF);
}
12

## Slide 13
05 — LIBRARY STRUCTURE
Why split into .h / .c files?
Reusable
Copy sbus.c/.h or ibus.c/.h into any new project without touching main.c
Clean main.c
main.c only calls the function — the implementation stays out of sight
Team-safe
Others can work on UART/other peripherals without colliding with this code
Standard practice
Every STM32CubeIDE project convention: one module = one .c/.h pair
#ifndef IBUS_H
#define IBUS_H
extern uint8_t ibusPacket[IBUS_PACKET_LEN];
void updateIbusPacket(uint16_t *channel, uint8_t num_of_channels);
#endif
13

## Slide 14
06 — WORKED EXAMPLE
SBUS: Input Channels → Output Packet
Input: 16 channels
channel[0..8] = 992 (center)
channel[9..15] = 172 (min)
Output: 25-byte packet (verified)
0f e0 03 1f f8 c0 07 3e f0 81
0f 7c e0 63 05 2b 58 c1 0a 56
b0 82 15 00 00
Verification checklist
Byte 0 = 0x0F (start marker) — correct
Byte 24 = 0x00 (end marker) — correct
Cross-checked against a standalone C simulation of the exact same packing loop
First attempt showed bit-7 flipped on odd-parity bytes — traced to the logic analyzer misreading the 9th (parity) bit, not a code bug
14

## Slide 15
06 — WORKED EXAMPLE
IBUS: Input Channels → Output Packet
Input: 14 channels
channel[0..8] = 1500 (center)
channel[9..13] = 1000 (min)
Output: 32-byte packet (verified)
20 40 dc 05 dc 05 dc 05 dc 05
dc 05 dc 05 dc 05 dc 05 dc 05
e8 03 e8 03 e8 03 e8 03 e8 03
1f f3
Verification checklist
Byte 0-1 = 0x20 0x40 (length + command) — correct
Checksum recomputed independently in Python: 0xF31F → bytes 1F F3 — matches exactly
All 14 channels decoded back to 1500 / 1000 correctly
First test run had channel[13] = 0 instead of 1000 — traced to a missing 14th value in the channel[] array initializer in main.c, not a bug in updateIbusPacket()
15

## Slide 16
07 — DEBUGGING LESSONS
Real build errors we hit (and fixed)
Missing semicolon after prototype
"old-style parameter declarations"
Every function prototype in a .h file needs a trailing ;
Function signature mismatch
"too few arguments to function"
main.c call and the .h declaration must have identical parameter lists
Variable defined twice
"multiple definition of sbusPacket"
extern in the .h announces it; exactly one .c file provides the real uint8_t array[]
Stale build artifacts
"undefined reference" after a fix
Project → Clean, then rebuild — incremental builds can link against old .o files
Unbalanced parentheses
"expected ';' before ')' token"
(uint8_t)(val >> 8) & 0xFF needs one more ( around (val >> 8) before & 0xFF
16

## Slide 17
WRAP-UP
Which one should you use?
Choose SBUS if…
• Your receiver / flight controller only supports SBUS (very common in FPV)
• You need all 16 channels
• You already have signal-inverter hardware on your PCB
• Slightly smaller frame (25 B) matters for your update rate budget
Choose IBUS if…
• Your receiver is FlySky (or IBUS-native)
• You want built-in error detection (checksum)
• You want to avoid extra inverter hardware
• 14 channels is enough for your setup
17

## Slide 18
Thank You